## Slide 1
EE6618: Three Dimension Video Technology
Dr. P.W.M. Tsang
eewmtsan@cityu.edu.hk
Room: G6505
Department of Electronic Engineering,
City University of Hong Kong

## Slide 2
Classical glass based stereoscopic 3D system
Glass free 3D system
Human 3D perception
The Art of Holography
Computer Generated Hologram
Binary and phase-only Holography
Realization of glass free 3D system
Realization of binary and phase-only holograms
Things to learn

## Slide 3
Interesting
Capable of realizing something from learnt materials
Learn a lot about classical and modern 3D technologies
Appreciate existing 3D technologies
Things to expect from this course

## Slide 4
Fundamental knowledge (e.g. convolution, sampling theorem, transform, etc.)
Lots of theories and equations
Things not to expect from this course
Questions for practicing calculations

## Slide 5
Interactive teaching emphasizing on 2 way communication (e.g. tutorial, mini-projects, test, etc.)
Lecturing, mostly on one way communication
Teaching modes
Both are important towards effective learning

## Slide 6
Mini-project on Realization of glasses free 3D system
Mini-project on Realization of binary/phase-only holograms
Assessment and examination
Demonstrations
Tests (2)
Examination (40%)
Course works (60%)

## Slide 7
Mini-project on Realization of glasses free 3D system
Mini-project on Realization of binary/phase-only holograms
Assessment
Demonstrations (may be replaced with reports)
Number of assignments: 3
1. Development a program with Matlab first miniproject.
2. Development a program with Matlab second miniproject.
3. Demonstration achievements in both miniprojects.
Miniprojects, and demonstrations (20%)
Details on date and format of assignments will be provided later

## Slide 8
Classical 3-D system
Digital holography
Assessment
Details on date and format of tests will be provided later
2 Tests on 2 major topics (40%)

## Slide 9
Film
The classical 2D Photography
L
R

## Slide 10
The classical 2D Photography
Film
L
R
Both eyes are viewing the same picture: No 3D effect
Question: Why do we observe 3D effect?

## Slide 11
Basic principles of 3D Perception
Human eyes have slightly different perception with the left and right eyes when viewing a scene image.
3D perception can be reconstructed if the image received by each eye can be recorded, and later presented to the corresponding eye.
L
R
To capture 3D scene, we need to capture what are observed by our 2, instead of a single eyes. In another words, need to capture 2 images.

## Slide 12
The 3D Movie craze in the 50’s
House of Wax, starring Vincent Price and directed by André de Toth, was released by Warner’s Brother in 1953. The movie is a remake of 1933's “Mystery of the Wax Museum”.
The movie was captured in dual interlocked 35 mm film
The 2 cameras are simulating human eyes, capturing what will be observed by our pair of eyes
Right camera
Left camera
Scene

## Slide 13
Basic principles of 3D Perception
L
R
What would happen if the pair of images are displayed directly? See the image on the left.
Unfortunately, a side by side arrangement of the L and R pictures cannot direct each picture to the corresponding eye.
In this example, we simply see 2 pictures.
While we can use 2 cameras to capture what is seen with our eyes, directly displaying them does not give the 3D effect. Why?

## Slide 14
Basic principles of 3D Perception
L
R
L
R
NOT
THE
SAME
How to reproduce this from the L and the R images?

## Slide 15
Practical 3D recording and viewing system
L
R
Left
image
Right image
Integrated picture
Left
image
Right
image
The left and right images are merged on the integrated picture, in a way that each will be diverted to the corresponding eyes.
But how?
Right projector
Left projector
The left and right images, are projected and overlapped on the screen, but then the viewer will see a double image instead of 3D perception

## Slide 16
Practical 3D recording and viewing system
L
R
Left
image
Right image
Integrated picture
Left
image
Right
image
The left and right images are merged on the integrated picture, in a way that each will be diverted to the corresponding eyes.
But how?
Solution: Filtering glasses
An optical filter is a planar medium that only allows certain component of optical wave to get through, and reject the rest.
The left and right images are pre-processed so that they can be separated in the future with an optical filter.

## Slide 17
A popular optical filter: Polarized medium
Light photons oscillates in all directions, and a polarizer only allows photons oscillating at certain angles to get through.

## Slide 18
A popular optical filter: Polarized medium
Light photons polarized in certain angle can pass through a polarizer with the same angle, but will be blocked by a polarizer of a different angle
PASS
BLOCK
We can use this property for filtering

## Slide 19
Polarized sheet
A popular optical filter: Polarized medium
2 or more images can be combined and separated in the future, if each is polarized with a different angle.
Film
Polarized sheet
Film
Visible only if the 2 polarizers are similar.

## Slide 20
Practical 3D recording and viewing system
L
R
Left
image
Right image
Integrated picture
Left
image
Right
image
Others of filters work on similar principle.
Lets have a look at an interesting photograph
0 degree
90 degree
0 degree
90 degree

## Slide 21
The classical 3D perception technology
Source: http://www.slidestudios.com/blog/wp-content/uploads/2009/08/3d-movie-audience.jpg

## Slide 22
The 3D Movie craze in the 50’s
House of Wax, starring Vincent Price and directed by André de Toth, was released by Warner’s Brother in 1953. The movie is a remake of 1933's “Mystery of the Wax Museum”.
The movie was shown in dual interlocked 35 mm projection with polarized glasses, presented in Widescreen
A pair of images, each with a different polarization, overlap on the screen
Source of photo: from movie “Mystery of the Wax Museum”.
Noted the pair of images are shown separately to illustrate the concept. They are actually overlapped on the screen.

## Slide 23
Principles of 3D Perception and Display
1. Polarized lens
Viewers have to wear a spectacles consisting of a pair of orthogonally polarized lens.
L
R
Screen
Left + Right images
0 degree
90 degree
Left image: 0 degree polarized
Right image: 90 degree polarized

## Slide 24
Principles of 3D Perception and Display
2. Anaglyph images
Viewers have to wear a spectacles consisting of a pair of chromaticlly opposite (e.g. Red and Blue) lens.
L
R
Screen
Left + Right images
Red
Blue
Left image: Red
Right image: Blue

## Slide 25
Principles of 3D Perception and Display
3. Shutter Glass: Time division multiplexing
Viewers have to wear a Shutter Glass spectacles that switches between left and right eye.
L
R
Right Image
Screen

## Slide 26
3. Shutter Glass: Time division multiplexing
Viewers have to wear a Shutter Glass spectacles that switches between left and right eye.
L
R
Left Image
Screen
Principles of 3D Perception and Display
One shutter glasses is required for each viewers

## Slide 27
4. Polarized screen
Viewers have to wear a spectacles consisting of a pair of orthogonally polarized lens.
L
R
0 degree
90 degree
Left image
Principles of 3D Perception and Display
Polarizer
Screen
0 degree polarized
Right image
90 degree polarized
Much cheaper than the shutter glasses. A more economical solution when there are numerous viewers.

## Slide 28
5. Cordless Polarized screen
Viewers have to wear a spectacles consisting of a pair of orthogonally polarized lens. Switching of polarizer driven by content.
Left image
Principles of 3D Perception and Display
Screen
Right image
Optical signal
Polarizer
Optical Sensor
Polarization
signal
Multiple viewing configurations: 3D stereoscopic, Pulfrich, and normal 2D.

## Slide 29
6. Retarder film screen
Viewers have to wear a spectacles consisting of a pair of orthogonally polarized lens.
L
R
0 degree
90 degree
Principles of 3D Perception and Display
Screen
Much cheaper than the shutter glasses or switched polarizer. Resolution is reduced.
Retarder film
L
R
L
R
L
R
L
R
L
R
L
R
L
R
L
R

## Slide 30
Contemporary 3D display technology
Before moving on with the lecture, lets have a look at an inspiring short video clip of 3D effect in theatre.

## Slide 31
Classical versus modern 3D Display
Classical stereoscopic 3D display
Monitor directs left image to left eye, and right image to right eye.
L
R
Left image
Right image
Screen

## Slide 32
Current Status of 3D Display
Projection mapping: A simple but realistic holographic/3-D effect on known geometry.
Projector

## Slide 33
Current Status of 3D Display
Cloaking: generating the illusion of invisibility
An opaque object will block part or whole of the scene from sight.
As such, the occluded object will become visible.
To achieve invisibility, an optical illusion is needed to generate the effect of light passing through the occluded object. this can be achieved with projection mapping, a technology that is invented in Japan at early 2000.

## Slide 34
Current Status of 3D Display
Cloaking: generating the illusion of invisibility
Projector
Camera

## Slide 35
Current Status of 3D Display
Aerial image projection is well known in the art for creating the illusion of a 3D image floating in space. This class of systems employs optical elements such as mirrors, and beam-splitters, etc. to project an image of an object onto a plane that is transparent to the viewers.
Projector/Display
Half mirror
Viewer
Object beam
Virtual image
Floating image

## Slide 36
Current Status of 3D Display
Sega Time Traveler arcade game (1991)
“Time Traveler or Hologram Time Traveler is a stereographic laserdisc FMV arcade game released in 1991 by Sega and designed by Dragon's Lair creator Rick Dyer. It is called the "World's First Holographic Video Game.” www.wikipedia.com

## Slide 37
Current Status of 3D Display
The HoloCube 3D Projection Box
“Measuring about 20-inches square, the Holocube packs a 40GB hard drive for storing up to 18 hours of compressed video, which can magically float at 1080i resolution within the cube at the flick of a switch.” www.engadget.com

## Slide 38
Current Status of 3D Display
Holographic aerial projector

## Slide 39
Current Status of 3D Display
“Danish company ViZoo developed the Cheoptics360, a 360 degree holographic video display system.” www.i4you.com
Vizoo Cheoptics 360

## Slide 40
Current Status of 3D Display
IO2 Technology: M3 Heliodisplay
“The Heliodisplay is a free-space display developed by IO2 Technology. A projector is focused onto a layer of mist in mid-air, resulting in a two-dimensional display that appears to float. This is similar in principle to the cinematic technique of rear projection.” www.wikipedia.com

## Slide 41
Current Status of 3D Display
Rotating mirror by the ICT Graphics Laboratory at the USC
Projecting high speed video onto a rapid rotating mirror, hence creating the illusion of a volumetric 3D image.
http://gl.ict.usc.edu/Research/3DDisplay/

## Slide 42
Current Status of 3D Display
3D via Laser Plasma Emission Technology
Using focused laser beam to produce plasma emission at a point. A scanning mirror steer the emission point in the 3D space

## Slide 43
Current Status of 3D Display
3D mirage Technology

## Slide 44
Current Status of 3D Display
3D floating image based on concave mirror

## Slide 45
Current Status of 3D Display
Volumetric Display
Layered volumetic display based on persistence of vision (POV)
HoloBlade
LED cube
Mechanical pistons
Hanging strings

## Slide 46
Current Status of 3D Display
Virtual Reality (VR) and Augmented Reality (AR)
VR: Presenting synthetic (usually computer generated) visual image to the eye
AR: Superimpose synthetic visual image to a physical scene
Hybrid AR/VR: Same as VR, but the background image is derived from a physical scene

## Slide 47
Current Status of 3D Display
Typical Virtual Reality (VR) system
VR: Presenting synthetic (usually computer generated) visual image to the eye
Micro-display
Focusing lens
Video images
Example: Oculus Rift
3D perception by showing left and right images on the corresponding micro-displays

## Slide 48
Current Status of 3D Display
Low Cost Virtual Reality (VR)
VR: Presenting synthetic (usually computer generated) visual image to the eye
Mobile phone
Focusing lens
Examples:
Samsung gear
Google Cardboard
Content example:
X3DOM

## Slide 49
Current Status of 3D Display
Augmented Reality (AR)
AR: Superimpose synthetic visual image to a physical scene
Transparent
glass
Prism
Projector
Example:
Google glass (single channel)
Metavision (Stereoscopic)
Microsoft Holo-lens (Stereoscopic)

## Slide 50
Current Status of 3D Display
Virtual/Augmented Reality
Camera captures the physical scene, and present the image to the eyes together with synthetic contents
Mobile phone
Focusing lens
Camera
Example:
Augmented Apps

## Slide 51
Current Status of 3D Display
Virtual Reality with X3DOM (www.x3dom.org)
A simple and friendly web based platform for displaying 3D computer graphics (CG) models.
Generate the standard html web template below.
Embedded the codes on 3D model.
View the result on a standard browser (e.g. Firefox).
Observe the 3D model from different viewing angle with the pointing devices (e.g. mouse).
<html>
<head>
<title>My first X3DOM page</title>
<script type='text/javascript' src='http://www.x3dom.org/download/x3dom.js'> </script>
<link rel='stylesheet' type='text/css' href='http://www.x3dom.org/download/x3dom.css'></link>
</head>
<body>
<h1>Hello, X3DOM!</h1>
<p>
This is my first html page with some 3d objects.
</p>
</body>
</html>

## Slide 52
Current Status of 3D Display
Virtual Reality with X3DOM (www.x3dom.org)
Generate the standard html web template below.
Embedded the codes on 3D model.
View the result on a standard browser (e.g. Firefox).
Observe the 3D model from different viewing angle with the pointing devices (e.g. mouse).
<x3d width=‘100px' height=‘100px'>
<scene>
<shape>
<appearance>
<material diffuseColor='1 0 0'></material>
</appearance>
<box></box>
</scene>
</x3d>
Rotate with mouse

## Slide 53
Current Status of 3D Display
Virtual Reality with X3DOM (www.x3dom.org)
Generate 2 views of the same model.
Place one on the left, and the other on the right.
Display the result on a standard browser (e.g. Firefox).
Observe the image pair with the VR headset
<x3d width=‘100px' height=‘100px'>
<scene>
<transform translation='-1.5 0 0'>
<shape>
<appearance>
<material diffuseColor='1 0 0'></material>
</appearance>
<box></box>
</shape></transform>
<transform translation='1.5 0 0'>
<shape>
<appearance>
<material diffuseColor='1 0 0'></material>
</appearance>
<box></box>
</shape></transform>
</scene>>
</x3d>
Lots of examples, including VR, are available in the website. Please learn how to build simple VR models for the headset.

## Slide 54
Current Status of Desktop 3D Display
Lens Free Multiple Views Stereoscopic 3D Monitor
Monitor Reconstructs multiple views before spectators.
L
R
Screen
V1
V2
V3
V4
V5
V6
V7
Typical number of views: 3 to 9.
Lenticular lens array
or barrier

## Slide 55
Current Status of Desktop 3D Display
Lens Free Multiple Views Stereoscopic 3D Monitor
Monitor Reconstructs multiple views before spectators.
Screen
V1
V2
V3
V4
V5
V6
V7
Lenticular lens array
or barrier
v7
v6
v5
v4
v3
v2
v1

## Slide 56
Image Acquisition and processing
Multiple cameras are required to capture and store the scene.
1. How to store?
2. How to compress?
3. Compatibility problem.
4. Storage media.
5. Broadcast media
6. Real Time 3D Display
Major issues to consider

## Slide 57
Typical approach adopted to date
1. A computer is needed
2. Tedious process
3. Fast Processor required
4. Higher Cost
Issues to consider
3D Monitor
V1
V2
V3
V4
V5
V6
V7
3D File
Renderer
1. Digitize and store multi-view images into a computer.
2. Create virtual 3D scenes with graphical software (e.g. 3DMAX)
5. Bulky setup

## Slide 58
Typical approach adopted to date
1. 3D camera is needed
2. Tedious process
3. Fast Processor required
4. Higher Cost
Issues to consider
3D Monitor
V1
V2
V3
V4
V5
V6
V7
2D+Depth
Renderer
1. 2D + Depth: Capture intensity and depth of each picture frame
2. Generate multi-view images.

## Slide 59
A simplified framework: Static N-tile format
Multiplexer
Single
N-tile image
Process like an ordinary
2D picture

## Slide 60
Modulator
PAL signal
Broadcast via existing TV channels
Store in Bluray, DVD, VCD, VCR, etc.
Compress with MPEG, JPEG2000, etc.
A simplified framework: Static N-tile format

## Slide 61
Renderer
3D Monitor
V1
V2
V3
V4
V5
V6
V7
A simplified framework: Static N-tile format

## Slide 62
Problems of the simplified framework
1. Poor resolution: each view is downsampled
3. Lack of hardware and software solutions for real time operations
2. Degradation in 3D perception
Simply speaking, there are lots of problems remain unsolved.

## Slide 63
Nevertheless, the N-tile format is a viable solution
Video Capturing
Integration
Visual Quality Enhancement
DVD
VCD
VCR
MPEG
PAL
NTSC
Blu-ray
DTT
Existing Video Chains
3D video acquisition and Production
3D Display
3D Decoder
Multi-views generation
Display
Integration of 3D video in existing video chains

## Slide 64
Potential of 3D Display System
1. Advertising companies
3. Conference and exhibitions organizers
2. Tourism companies
4. The entertainment industries
The 3D display system will create a significant impact on the traditional channel of conveying video and graphic contents. Our technology will enable 3D contents to be produced and display at a very competitive cost based on existing video equipment and video chains.
For example, potential applications of 3D Kiosks

## Slide 65
The Future
Lets see from the video clip what is anticipated in the future

## Slide 66
Photography vs Holography
Photography: Recording and reproduction of a single 2D perspective of a 3D scene on a 2D media (such as film).
Pin-hole
Photo-film
Photo-film
Opaque
The pin-hole only allows light waves from a single view of the scene to go through. The rest are blocked. The light beam from each point on the scene hits on a unique spot on the photo-film, and its intensity is recorded on the photo-emulsion at that particular point.

## Slide 67
Photography vs Holography
Apparently, removing the pin-hole will allow all the light wave from different views of the scene to get through.
But then the light wave from all viewing directions will be accumulated on the photo-film through scalar addition. Once added, light wave from individual viewing direction cannot be separate in the future. The image on the photo-film is a chaotic pattern that bears no resemblance to the original scene.
Photo-film

## Slide 68
Holography
Hologram: Same principle, but the complex optical waves are added up
The holographic signal H(x,y) is complex (with magnitude and phase when a light beam arrive at a point on the photo-film.
Photo-film
(Hologram)

## Slide 69
Holography
When the actual object is removed, H(x,y) reproduced all the recorded light waves, and the observer will have the illusion of seeing the original object image.
However, photo-film can only record the magnitude (i.e. intensity) of the light wave.
Hologram

## Slide 70
Optical Holography
Hologram: Recording and reproduction of 3D scene on and from a 2D media (such as film).
Laser
Hologram
Laser
Hologram

## Slide 71
Computer Generated Holography
Given a discrete, 3-D image, a digital hologram can be generated numerically as the real part of the product of the object and a planar reference waves. The 3-D image can be reconstructed from the hologram afterwards.
Computer Generated Hologram (CGH): Generation of holograms numerically from three dimensional (3-D) models that do not actually exist in the real world.
3D Computer graphic model
Computer
Hologram file
Printer/Display
hologram

## Slide 72
Computer Generated Holography
3D Object
Space
point
Object
Hologram
z
y
x
1. Compute the diffracted wave from each individual point.
2. Sum up the contributions of all the points to form the hologram

## Slide 73
Computer Generated Holography
3D Object
Space
point
Object
Hologram
z
y
x
u
v
A single point

## Slide 74
Computer Generated Holography
3D Object
Space
point
Object
Hologram
z
y
x
u
v
All the points

## Slide 75
Problems with Digital Holography
A digital Hologram is complex and cannot be printed on a photo-film.
Existing display devices (SLM) can only display either magnitude or phase component
Generating a hologram involves very heavy amount of computation.

## Slide 76
Other problems with Digital Holography
1. This walkthrough only provides a brief glimpse on the 3D technology
2. There are plenty of details.
3. Past, present, and emerging technologies can work in synergy.