## Slide 1
3D for the public viewers
Binocular (perceivable with 2 eyes)
Left
Right
Optical
Splitter
Left eye
Right eye
How to direct the left and right images to the correct eye?

## Slide 2
Left picture
Blue component only
Right picture
Red component only
Projection
Transmission
Wavelength
650nm
475nm
475nm
Blue filter
Anaglyph
Red filter
Red filter
Blue filter

## Slide 3
Polarized glasses based Stereoscopic 3D
Left picture
polarized at 0 degree
Right picture
polarized at 90 degree
0 degree polarizer
90 degree polarizer
Usual approach: Display left and right eyes images on the same screen, and utilizes polarized glasses to direct each image to the corresponding eye.
Malus’s law: Intensity is attenuated by the square of the cosine of the angle between the polarization directions of the light and the polarizing filter, as
Hence, the viewing level must be strictly horizontal to avoid ghosting.
Projection

## Slide 4
Circular Polarizing filter
Circular Polarizing filter: polarization rotates clockwise or anticlockwise after passing through it.
Unpolarized light
http://upload.wikimedia.org/wikipedia/commons/d/d1/Circular.Polarization.Circularly.Polarized.Light_Left.Hand.Animation.305x190.255Colors.gif
90o
0o
Anticlockwise polarizer
Unpolarized light
90o
0o
Clockwise polarizer
Polarizing angle

## Slide 5
Circular Polarizing filter
Circular Polarizing filter: polarization rotates clockwise or anticlockwise after passing through it.
Unpolarized light
90o
0o
90o
0o
Anticlockwise polarized light
Anticlockwise polarizer
Clockwise polarizer
Block

## Slide 6
Circular Polarized glasses
based Stereoscopic 3D
Left picture
Clockwise polarized
Right picture
Anticlockwise polarized
Clockwise polarizer
Anticlockwise polarizer
Using circular polarized images and glasses avoid the constraint on level viewing. Adopted in modern 3D movies and TV signals.
Projection

## Slide 7
Stereoscopic 3D on TV
Time division multiplexing
Left image
Right image
Left and right images are shown in the odd and even ( or even and odd) frames, respectively.
L
R
L
R
L
R
Lower brightness as glasses are only conducted at 50% of time. Expensive and bulky active shutter glasses.
Synchronized to respective field
Active shutter glass

## Slide 8
Film-type Patterned Retarder: LG
Checker sampling technology
Left eye picture (cw-cp)
Right eye picture (acw-cp)
No flickering, brighter image. Low cost glasses.
A film with circular polarizing element is placed on each pixel. Left and right pixels have different direction of polarization (cw-cp and acw-cp).
Stereoscopic 3D on TV
Picture resolution is lowered by a factor of 2.
Clockwise circular polarizer
Anticlockwise circular polarizer

## Slide 9
Glass free (naked eye) 3D viewing
Origin: Classic lenticular 3D photographs.
Basic concept: Interleave 2 or more views on the screen.
Overlay a lenticular lens array, or a parallax barrier.
The lens array or barrier deflects each view to its respective direction.
Left Eye
Right Eye
Interlaced image
Lenticular lens array
Left image pixel
Right image pixel
Interleaving and viewing of a pair of stereoscopic images

## Slide 10
Glass free (naked eye) 3D viewing
Interleaving left and right images on the screen can be described as a decimation and interpolation process.
1. Each image is decimated into a new image that is half of its original width. 2. The decimated images are interpolated and interleave on the screen.
Decimation, interpolation, and Interleaving of a pair of stereoscopic images
A
A
Decimation
Interpolation
A
Decimation leads to distortion which cannot be fully recovered with interpolation.
Blank strip filled by the second image

## Slide 11
Decimation
x(n)
M
y(n)
-3
-2
-1
0
1
2
3
4
-4
-3
-2
-1
0
1
2
3
4
e.g. M = 2
x(n)
x’(n)
y(n)
-4
Something is lost!
M is the decimation factor

## Slide 12
Decimation in 2 steps: 1st step
x(n)
x’(n)
x’(n) =
x(n) n = 0 , +M , +2M , +3M , +4M, ...
0 otherwise
(1)

## Slide 13
Decimation: 1st step
(1)
i(n) is a periodic impulse train that can be expressed as
(2)
i(n)
0
M
2M
-2M
-M

## Slide 14
Decimation: 1st step
(1)
(2)
(3)

## Slide 15
Decimation: 2nd step
x(n)
x’(n)
y(n)
y(n) = x’(Mn)
(4)
According to equation (3)
(5)

## Slide 16
Decimation: 2nd step
Converting the decimated signal yto frequency space with discrete Fourier transform:
The frequency spectrum is scaled by a factor M. Frequency axis is lengthened.
There are M copies (replicas) of the original base-band (scale in width).
The replicas are located at .
If the bandwidth of the signal exceeds , the replicas overlap with each other, leading to aliasing error.
The frequency spectrum of x is .

## Slide 17
Decimation: illustration
x(n)
x’(n)
y(n)
0
/4
/4
/2
/4

/4
/2
/4

/4
/2
/4

0
/4
/4
/2
/4

/4
/2
/4

/4
/2
/4

0
/4
/4
/2
/4

/4
/2
/4

/4
/2
/4

M=4

## Slide 18
Interpolation
x(n)
M
y(n)
-4
-3
-2
-1
0
1
2
3
4
e.g. M = 2
y(n)
-2
-1
0
1
2
x(n)

## Slide 19
Interpolation
x(n)
M
y(n)
(6)
y(n) =
x(n/M) n = 0 , +M , +2M , +3M , ...
0 otherwise
The frequency spectrum is scaled by a factor M. The frequency scale is compressed.

## Slide 20
Interpolation
0
/4
/4
/2
/4

/4
/2
/4

/4
/2
/4

0
/4
/4
/2
/4

/4
/2
/4

/4
/2
/4

M=4
No change other than a scaling of the frequency axis.

## Slide 21
Glass free (naked eye) 3D viewing
Does it works on monitor?
A pixel on the screen
Intuitively, we can simply interleave the pixels on the monitor in alternating left and right manner.

## Slide 22
Usual pixel arrangement
Glass free (naked eye) 3D viewing
Early product by Sharp: Stereoscopic (2 views) with rainbow moiré pattern
Interleaving and viewing multi-view images
Left pixel
Right pixel
Slight difference in viewing positions capture incomplete pixel components

## Slide 23
Glass free (naked eye) 3D viewing
Avoiding rainbow moiré patterns: Rotate screen by 90 degree.
Left Eye
Right Eye
Interlaced images
Lenticular lens array
Interleaving and viewing multi-view images
Left pixel
Right pixel
Slight difference in viewing positions capture same pixel components. Very poor resolution for large number of views.
Rotated pixel arrangement

## Slide 24
Glass free (naked eye) 3D viewing
with Auto-stereoscopic monitor
4
5
6
7
1
2
3
4
5
6
7
1
2
3
4
5
6
7
1
2
3
4
5
6
7
1
2
3
4
5
6
7
1
2
3
4
5
6
7
1
2
3
4
5
6
7
1
2
3
4
5
6
7
1
2
3
Lenticular lens array
Magnified view of one lens column
Very poor horizontal resolution

## Slide 25
Glass free (naked eye) 3D viewing
with Auto-stereoscopic monitor
Rotating the lenticular lens array by certain degree

## Slide 26
2
2
4
6
2
4
6
2
4
6
1
3
5
1
3
5
1
3
5
6
2
4
6
2
4
6
2
4
5
1
3
5
1
3
5
1
3
4
6
2
4
6
2
4
6
2
2
2
4
6
2
4
6
2
4
6
1
3
5
1
3
5
1
3
5
6
2
4
6
2
4
6
2
4
5
1
3
5
1
3
5
1
3
4
6
2
4
6
2
4
6
2
2
2
4
6
2
4
6
2
4
6
1
3
5
1
3
5
1
3
5
6
2
4
6
2
4
6
2
4
5
1
3
5
1
3
5
1
3
4
6
2
4
6
2
4
6
2
Glass free 3D viewing
Slant Lenticular technology
Philips patent: US6,064,424 (May 2000)
Distribute resolution degradation to horizontal and vertical directions
View 2
View 3
View 4

## Slide 27
An early attempt to compress 3D stereoscopic sequences has been made by the MPEG with the incorporation of the Multiview Profile (MVP) [1][2] into the existing MPEG II standard. The approach is largely an extension of the temporal scalability, but so far the MVP has not been adopted as a commercially available service.
[1] M. Tanimoto and T. Fuji, “Utilization of inter-view correlation for multiple view video coding”, ISO/IEC JTC1/SC29/WG11 M11014, July 2004.
[2] H. Wang, et al, “Using inter-view prediction for multi-view video compression”, ISO/IEC JTC1/SC29/WG11 M10512, Mar. 2004.
Packaging and distribution of muti-view signals

## Slide 28
Another approach has been developed by the Mitsubishi Electrical Research Laboratory. Its technology, known as the “simulcast” compresses individual views of video sequences with MPEG II and dispatches them via separate channel.
At the receiver they were decoded and integrated and shown on the 3D display. The method is straightforward, compatible with existing Digital Broadcasting infrastructure.
However the system is extremely complicated, requiring multiple PCs and high bandwidth networks on both the transmission and receiving sides.
Packaging and distribution of muti-view signals

## Slide 29
The “Advanced Three-dimensional Television System Technologies (ATTEST) project [3] of the European Information Society Technologies (IST) aims at the development of a complete 3D-video chain including content creation, coding, transmission and display.
“Depth Image Based Rendering” (DIBR) technology is adopted where a Three Dimensional Scene is encoded as a single view plus a depth map.
To allow backward compatibility to existing 2D digital television, the base layer is encoded with MPEG II and DVB standards. The depth map is transmitted in the enhancement layer with MPEG 2/4/7 standard providing a depth value for each pixel in the base layer. At the receiver, 3D views are generated from the 2D image of the base layer and the depth map of the enhancement layer.
[3] M.O. Beeck, “Towards an Optimized 3D Broadcast Chain”, Proc. SPIE 4864, Three-Dimensional TV, Video, and Display, 42 (November 1, 2002);
Packaging and distribution of muti-view signals

## Slide 30
it is unlikely that the compressed multi-view 3D data could be distributed directly in the same way as the existing channels and standards.
While it may be argued that technically, present standards and hardware solutions could always be changed to accommodate the newer technologies, such revolutions usually have to experience long period of incubation period before every components in the video chain could function collaboratively and survive in the consumer’s world.
Packaging and distribution of muti-view signals
StereoGraphics offers an alternative approach know as the “N-tiles”, a.k.a. the Hollywood Squares” format.
Images from cameras each capturing a view of the scene are down-sampled and juxtaposed as non-overlapped tiles into a single picture.
This enables multi-view images cav be processed in the same way as ordinary two dimensional pictures, and embedded into existing video chains.

## Slide 31
Packaging and distribution of muti-view signals: N-tile format

## Slide 32
Packaging and distribution of muti-view signals: N-tile format

## Slide 33
Packaging and distribution of muti-view signals: N-tile format
In general, though not mandatory, the number of cameras N is taken to be the square of an integer D, i.e.
W(n,x,y) is just an ordinary picture frame that can be modulated, compressed, broadcast and recorded by any existing standards.
At the receiving end, each view in W(n,x,y) is mapped to the corresponding sub-pixel in the auto-stereoscopic 3D monitor.

## Slide 34
Packaging and distribution of muti-view signals: N-tile format